## Slide 1: DATA MANIPULATION
Lecture slides are adapted/modified from slides provided by the textbook, Computer Science: An Overview by J. Glenn Brookshear and Dennis Brylow
publisher Pearson

## Slide 2: Data Manipulation
Computer Architecture
Machine Language
Program Execution
Arithmetic/Logic Instructions
Communicating with Other Devices
Other Architectures

## Slide 3: Computer Architecture

## Slide 4: Computer Architecture
Central Processing Unit (CPU) or processor
  Arithmetic/Logic unit versus Control unit
  Registers
    General purpose
    Special purpose
Bus
Motherboard

## Slide 5: CPU and main memory connected via a bus

## Slide 6: Motherboards
The motherboard
  is the main printed circuit board.
  contains the buses, or electrical pathways found in a computer. Buses allow data to travel among the various components.
  accommodates CPU, RAM, expansion slots, heat sink/fan assembly, BIOS chip, chip set, sockets, internal and external connectors, various ports, and the embedded wires that interconnect the motherboard components.
Notes: 1.1.2.1 Identify the names, purposes, and characteristics of motherboards
A motherboard is also known as the system board, the backplane, or the main board.
Sockets, internal and external connectors, and various ports are also placed on the motherboard.

## Slide 7: Central Processing Unit
The Central Processing Unit (CPU) is known as the brain of the computer. It is also referred to as the processor.
The CPU executes a program, which is a sequence of stored instructions.
Notes: 1.1.2.2 Identify the names, purposes, and characteristics of CPUs
Most calculations take place in the CPU. CPUs come in different form factors, each style requiring a particular slot or socket on the motherboard. Common CPU manufacturers include Intel and AMD.
The CPU socket or slot is the connector that interfaces between the motherboard and the processor itself.
The CPU executes a program, which is a sequence of stored instructions. Each model of processor has an instruction set, which it executes. The CPU executes the program by processing each piece of data as directed by the program and the instruction set. While the CPU is executing one step of the program, the remaining instructions and the data are stored nearby in a special memory called cache. There are two major CPU architectures related to instruction sets:
  Reduced Instruction Set Computer (RISC) – Architectures use a relatively small set of instructions, and RISC chips are designed to execute these instructions very rapidly.
  Complex Instruction Set Computer (CISC) – Architectures use a broad set of instructions, resulting in fewer steps per operation.

## Slide 8: Central Processing Unit
Some CPUs incorporate hyperthreading or hypertransport to enhance the performance of the CPU.
The amount of data that a CPU can process at one time depends on the size of the processor data bus.
Speed of the CPU is measured in cycles per second - megahertz (MHz) or gigahertz (GHz).
Overclocking is a technique used to make a processor work at a faster speed than its original specification.
Notes: 1.1.2.2 Identify the names, purposes, and characteristics of CPUs
With hyperthreading, the CPU has multiple pieces of code being executed simultaneously on each pipeline. To an operating system, a single CPU with hyperthreading appears to be two CPUs.
The speed of a CPU is rated in cycles per second. The speed of current CPUs is measured in millions of cycles per second, called megahertz (MHz), or billions of cycles per second, called gigahertz (GHz). This is also called the CPU bus or the front side bus (FSB). The wider the processor data bus width, the more powerful the processor is. Current processors have a 32-bit or a 64-bit processor data bus.
Overclocking is not a reliable way to improve computer performance and can result in damaging the CPU.
MMX enabled microprocessors can handle many common multimedia operations that are normally handled by a separate sound or video card. However, only software especially written to call MMX instructions can take advantage of the MMX instruction set.

## Slide 9: Central Processing Unit
The latest processor technology has resulted in CPU manufacturers finding ways to incorporate more than one CPU core onto a single chip.
  Dual Core CPU - Two cores inside a single CPU
  Triple Core CPU - Three cores inside a single CPU
  Quad Core CPU - Four cores inside a single CPU
  Hexa-Core CPU - Six cores inside a single CPU
  Octa-Core CPU - Eight cores inside a single CPU
Notes: 1.1.2.2 Identify the names, purposes, and characteristics of CPUs
The latest processor technology has resulted in CPU manufacturers finding ways to incorporate more than one CPU core onto a single chip. Many CPUs are capable of processing multiple instructions concurrently:
  Single Core CPU – One core inside a single CPU chip that handles all of the processing capability. A motherboard manufacturer may provide sockets for more than one single processor, providing the ability to build a powerful, multi-processor computer.
  Dual Core CPU – Two cores inside a single CPU chip in which both cores can process information at the same time.
  Triple Core CPU – Three cores inside a single CPU that is actually a quad-core processor with one of the cores disabled.
  Quad Core CPU – Four cores inside a single CPU in which all cores can process information simultaneously for enhanced software applications.
  Hexa-Core CPU - Six cores inside a single CPU
  Octa-Core CPU - Eight cores inside a single CPU

## Slide 10: The Arithmetic/Logic Unit
Subsystem that performs addition, subtraction, and comparison for equality
Components
  Registers, interconnections between components, and the ALU circuitry
Register
  Storage cell that holds the operands of an arithmetic operation and holds its result
Bus
  Path for electrical signals

## Slide 11: The Arithmetic/Logic Unit
Registers are similar to RAM with following minor differences
  They do not have a numeric memory address but are accessed by a special register designator such as A, X or R0
  They can be accessed much more quickly than regular memory cells
  They are not used for general purpose storage but for specific purposes such as holding the operands for an upcoming arithmetic computations.
A typical ALU has 16, 32 or 64 registers.

## Slide 12: The Control Unit
Control unit
  Tasks: fetch, decode, and execute

## Slide 13: Machine Language

## Slide 14: Stored Program Concept
A program can be encoded as bit patterns and stored in main memory.
From there, the CPU can then extract the instructions and execute them.
In turn, the program to be executed can be altered easily.

## Slide 15: Terminology
Machine instruction: An instruction (or command) encoded as a bit pattern recognizable by the CPU
Machine language: The set of all instructions recognized by a machine

## Slide 16: Machine Language Philosophies
Reduced Instruction Set Computing (RISC)
  Few, simple, efficient, and fast instructions
  Examples: PowerPC from Apple/IBM/Motorola and ARM
Complex Instruction Set Computing (CISC)
  Many, convenient, and powerful instructions
  Example: Intel
Notes: AMD: Advanced Micro Devices
ARM: Advanced RISC Machine (low power consumption). Game controller, digital TV, ..

## Slide 17: Machine Instruction Types
Data Transfer: copy data from one location to another
Arithmetic/Logic: use existing bit patterns to compute a new bit patterns
Control: direct the execution of the program

## Slide 18: Adding values stored in memory

## Slide 19: Dividing values stored in memory

## Slide 20: An architecture of the machine

## Slide 21: Parts of a Machine Instruction
Op-code: Specifies which operation to execute
Operand: Gives more detailed information about the operation
  Interpretation of operand varies depending on op-code

## Slide 22: The composition of an instruction

## Slide 23: Decoding the instruction 35A7

## Slide 24: A Simple Machine Language
Op-code | Operand | Description
1 | RXY | LOAD reg. R from cell XY.
2 | RXY | LOAD reg. R with XY.
3 | RXY | STORE reg. R at XY.
4 | 0RS | MOVE R to S.
5 | RST | ADD S and T into R. (2’s comp.)
6 | RST | ADD S and T into R. (floating pt.)

## Slide 25: A Simple Machine Language
Op-code | Operand | Description
7 | RST | OR S and T into R.
8 | RST | AND S and T into R.
9 | RST | XOR S and T into R.
A | R0X | ROTATE reg. R X times.
B | RXY | JUMP to XY if R = reg. 0.
C | 0 | HALT.

## Slide 26: A Simple Machine Language
14A3: Load
  The contents of the memory cell located at address A3 to be placed in register 4.
20A3: Load
  The value A3 to be placed in register 0.
35B1: Store
  The contents of register 5 to be placed in the memory cell whose address is B1.
40A4: Move
  The contents of register A to be copied into register 4.

## Slide 27: A Simple Machine Language
5726: Add
  The binary values in registers 2 and 6 to be added and the sum placed in register 7.
634E: Add
  The values in registers 4 and E to be added as floating-point values and the result to be placed in register 3.

## Slide 28: A Simple Machine Language
7CB4: Or
  The result of ORing the contents of registers B and 4 to be placed in register C.
8045: And
  The result of ANDing the contents of registers 4 and 5 to be placed in register 0.
95F3: Xor
  The result of XORing the contents of registers F and 3 to be placed in register 5.
A403: Rotate
  The contents of registers 4 to be rotated 3 bits to the right in a circular fashion.

## Slide 29: A Simple Machine Language
B43C:
  Compare the contents of register 4 with the contents of register 0.
  If equal, the pattern 3C would be placed in the program counter so that the next execution executed would be the one located at that memory address.
  Otherwise, nothing would be done.
C000:
  Stop program execution.

## Slide 30: An encoded version of the instructions

## Slide 31: Quiz
The following are instructions written in the above simple machine language. Rewrite in English.
  368A
  BADE
  803C
  40F4

## Slide 32: Quiz
What is the difference between the instructions 15AB and 25AB in the simple machine language?

## Slide 33: Quiz
Here are some instructions in English. Translate each of them into the simple machine language.
  LOAD register number 3 with the hexadecimal 56.
  ROTATE register number 5 three bits to the right.
  AND the contents of register A with the contents of register 5 and leave the result in register 0.

## Slide 34: Quiz
Here are some instructions in English. Translate each of them into the simple machine language.
  LOAD register number 3 with the hexadecimal 56.
  2356
  ROTATE register number 5 three bits to the right.
  A503
  AND the contents of register A with the contents of register 5 and leave the result in register 0.
  80A5

## Slide 35: Program Execution

## Slide 36: Program Execution
Controlled by two special-purpose registers
  Program counter: address of next instruction
  Instruction register: current instruction
Machine Cycle
  Fetch
  Decode
  Execute

## Slide 37: The machine cycle

## Slide 38: Decoding the instruction B258

## Slide 39: A program stored in main memory

## Slide 40: The fetch step of the machine cycle

## Slide 41: The fetch step of the machine cycle

## Slide 42: Arithmetic/Logic Instructions

## Slide 43: Arithmetic/Logic Operations
Logic: AND, OR, XOR
  Masking
Rotate and Shift:
  circular shift (rotation)
  logical shift
  arithmetic shift
Arithmetic: add, subtract, multiply, divide
  Precise action depends on how the values are encoded (two’s complement versus floating-point).

## Slide 44: Masking

## Slide 45: Circular shift

## Slide 46: Logical shift

## Slide 47: Quiz
What logical operation together with what mask can you use to change ASCII codes of lower characters to uppercase? What about uppercase to lowercase?

## Slide 48: Quiz
Identify both the mask and the logical operation needed to accomplish each of the following objectives:
Put 1s in the upper 4 bits of an 8-bit pattern without disturbing the other bits.
Complement the most significant bit of an 8-bit pattern without changing the other bits.
Complement a pattern of 8 bits.
Put a 0 in the least significant bit of an 8-bit pattern without disturbing the other bits.

## Slide 49: Quiz
Identify both the mask and the logical operation needed to accomplish each of the following objectives:
Put 1s in the upper 4 bits of an 8-bit pattern without disturbing the other bits.
  OR 1111 0000
Complement the most significant bit of an 8-bit pattern without changing the other bits.
  XOR 1000 0000
Complement a pattern of 8 bits.
  XOR 1111 1111
Put a 0 in the least significant bit of an 8-bit pattern without disturbing the other bits.
  AND 1111 1110

## Slide 50: Quiz
Identify both the mask and the logical operation needed to accomplish each of the following objectives:
Put 1s in all but the most significant bit of an 8-bit pattern without disturbing the most significant bit.
Filter out all of the green color component from an RGB bitmap image pixel in which the middle 8 bits of a 24-bit pattern store the green information.
Invert all of the bits in a 24-bit RGB bitmap
Set all the bits in a 24-bit RGB bitmap pixel to 1, indicating the color “white”.

## Slide 51: Quiz
Identify a logical operation (along with a corresponding mask) that, when applied to an input string of 8 bits, produces an output string of all 0s if and only ifs the input string is 1000 0001.

## Slide 52: Communicating with Other Devices

## Slide 53: Communicating with Other Devices
Controller: An intermediary apparatus that handles communication between the computer and a device
  Specialized controllers for each type of device
  General purpose controllers (USB and FireWire)
Port: The point at which a device connects to a computer
Memory-mapped I/O: CPU communicates with peripheral devices as though they were memory cells

## Slide 54: Controllers attached to a machine’s bus

## Slide 55: A conceptual representation of memory-mapped I/O

## Slide 56: Communicating with Other Devices
Direct memory access (DMA): Main memory access by a controller over the bus
Von Neumann Bottleneck: Insufficient bus speed impedes performance
Handshaking: The process of coordinating the transfer of data between components

## Slide 57: Communicating with Other Devices
Parallel Communication: Several communication paths transfer bits simultaneously.
Serial Communication: Bits are transferred one after the other over a single communication path.

## Slide 58: Data Communication Rates
Measurement units
  Bps: Bits per second
  Kbps: Kilo-bps (1,000 bps)
  Mbps: Mega-bps (1,000,000 bps)
  Gbps: Giga-bps (1,000,000,000 bps)
Bandwidth: Maximum available rate

## Slide 59: Quiz
Assume that the machine (using the simple machine language as described) uses memory-mapped I/O and that the address B5 is the location within the printer port to which data to be printed should be sent.
If register 7 contains the ASCII code for the letter A, what machine language instruction should be used to cause that letter to be printed at the printer?
If the machine executes a million instructions per second, how many times can this character be sent to the printer in one second?

## Slide 60: Quiz
Assume that the machine (using the simple machine language as described) uses memory-mapped I/O and that the address B5 is the location within the printer port to which data to be printed should be sent.
If the printer is capable of printing five traditional pages of text per minute, will it be able to keep up with the characters being sent to it in (b)?

## Slide 61: Quiz
Estimate how long it would take to transfer a 250-page novel (about 500,000 characters) encoded in 16-bit Unicode characters at a transfer rate of 54Mbps.

## Slide 62: What’s on the Outside of the Box?

## Slide 63: What’s on the Outside of the Box?
Connectors on a notebook may vary
Notes: This is Figure 2.29.

## Slide 64: Universal serial bus
USB (universal serial bus) ports
  Connects up to 127 peripheral devices
  USB 2.0 (high-speed USB)—fully compatible with USB 1.1 products, cables, and connectors
  Designed to replace older parallel and serial ports
  Connects a variety of devices to the computer, including:
    Keyboards
    Mice
    Printers
    Digital cameras

## Slide 65: Universal serial bus
USB 2.0
  Uses an external bus
  Supports data transfer rates of 480 Mbps between the computer and the peripheral device
  Supports hot swapping—ability to connect and disconnect devices without shutting down the computer
  Plug-and-play (PnP)—allows computers to automatically detect the device when you plug it in
USB 3.0 (2008): 5Gbps
USB 3.1 (2013): 10Gbps
USB hub
  Device that plugs into existing USB port
  Contains four or more additional ports
Notes: This is Figure 2.20.

## Slide 66: FireWire
FireWire (1395 ports)
  Created by Apple in 1995
  IEEE 1394 Higher Performance Serial Bus, also known as Sony i.Link
  Offers high-speed connections for dozens of peripheral devices (up to 63)
  Enables hot swapping and PnP
  Data transfer rates of FireWire
    FireWire 400—400 Mbps
    FireWire 800—800 Mbps
    Declared “dead” by Steve Jobs.
Notes: This is Figure 2.20.

## Slide 67: Video connectors
VGA (video graphics array)
  15-pin male connector—works with standard monitor cables
  Transmits analog video signals
  Used for legacy technology cathode ray (CRT) monitors
DVI (Digital visual Interface) port—lets LCD monitors use digital signals
Onboard video—video circuitry built into the motherboard where the video connector is on the back of the system unit case
Notes: This is Figure 2.20.

## Slide 68: HDMI
High-Definition Multimedia Interface
  A video/audio interface for transmitting uncompressed video data, and compressed/uncompressed audio data.
  Digital replacement for analog video standards.
  Designed: 2002 (7 companies).
  HDMI 2.1: 48Gbps.
  Newer version: 3D, Ethernet data connection, Consumer Electronics Control (CEC) extensions.

## Slide 69: Additional connectors
Telephone
Network
PC card slot
  PC card
  ExpressCard
Sound card
Game card
TV/sound capture board

## Slide 70: What’s on the Outside of the Box?
Legacy technology
  Older technology that is being phased out
    Examples:
        Serial ports
        Parallel ports
        PS/2 ports
        SCSI (small computer system interface) ports

## Slide 71: Other Architechtures

## Slide 72: Other Architectures
Technologies to increase throughput:
  Pipelining: Overlap steps of the machine cycle
  Parallel Processing: Use multiple processors simultaneously
    SISD: No parallel processing
    MIMD: Different programs, different data
    SIMD: Same program, different data

## Slide 73: Pipelining

## Slide 74: Parallel processing
  Method where more than one processor performs at the same time—faster processing