## Slide 1: NETWORKING AND THE INTERNET
Lecture slides are adapted/modified from slides provided by the textbook, Computer Science: An Overview by J. Glenn Brookshear and Dennis Brylow
publisher Pearson

## Slide 2: Contents
Network Fundamentals
The Internet
The World Wide Web
Internet Protocols
Security
Notes: http://www.kevinsworkbench.com/networking_quiz/study_guide.html

## Slide 3: Network Fundamentals

## Slide 4: Networks
Links multiple computer systems and enables them to share data and resources

## Slide 5: Network Classifications
Scope
  Personal area network (PAN)
  Local area network (LAN)
  Metropolitan area (MAN)
  Wide area network (WAN)
Ownership
  Closed versus open
Topology (configuration)
  Bus (Ethernet)
  Star (Wireless networks with central Access Point)

## Slide 6: Network Fundamentals
Local Area Network (LAN)
  Uses cables, radio waves, or infrared signals
  Links computers in a limited geographic area
Wide Area Network (WAN)
  Uses long-distance transmission media
  Links computer systems a few miles or thousands of miles
  Internet is the largest WAN
Metropolitan Area Network (MAN)
  Designed for a city
  Larger than a LAN, smaller than a WAN

## Slide 7: Network Fundamentals
Campus Area Network (CAN)
  Several LANs located in various locations on a college or business campus
  Smaller than a WAN
  Use devices such as switches, hubs, and routers
Personal Area Network (PAN)
  Network of an individual’s own personal devices
  Usually within a range of 32 feet
  Usually use wireless technology

## Slide 8: Network Fundamentals
Node
  Any device connected to a network
Logical address
  Unique name assigned to each node on the network
Physical address
  Unique numeric that identifies each node on the network built into the hardware
Network interface card (NIC)
  Expansion board or adapter that provides a connection between the computer and the network
  Notebook computers have wireless NICs

## Slide 10: Network Fundamentals
USB wireless network adapter
  Plugs into a USB port
  Usually provides an intuitive graphical user interface (GUI) for easy configuration
Wireless PC card adapter
  About the size of a credit card
  Inserted into a slot on the side of most notebooks and netbooks
  Has built-in WiFi antenna that provides wireless capability
  LED lights that indicate whether the computer is connected

## Slide 11: Network Fundamentals
USB wireless network adapter
  Plugs into a USB port
  Usually provides an intuitive graphical user interface (GUI) for easy configuration
USB dongle
  Device inserted into a USB port that adds additional features to the base system
  Examples: enabling network connectivity and increasing RAM
Wireless PC card adapter
  About the size of a credit card
  Inserted into a slot on the side of most notebooks and netbooks
  Has built-in WiFi antenna that provides wireless capability
  LED lights that indicate whether the computer is connected

## Slide 12: Connecting Networks
Repeater: Extends a network
Bridge: Connects two compatible networks
Switch: Connects several compatible networks
Router: Connects two incompatible networks resulting in a network of networks called an internet

## Slide 13: Network Fundamentals
Hub
  Joins multiple computers together in a single network
  Does not manage traffic between the connections
Switches
  Filter and forward data between nodes
  Are similar to routers but work within a single network
Routers
  Connect two or more networks
  Inspect the source and target of a data package
  Determine the best route to transmit data

## Slide 14
Notes: https://www.amazon.com/TP-Link-Ethernet-Splitter-Unmanaged-TL-SF1008D/dp/B0034CL3MA/ref=pd_sim_147_3?_encoding=UTF8&pd_rd_i=B0034CL3MA&pd_rd_r=1a379213-cb03-11e8-80f2-5f2216a1cfe5&pd_rd_w=Y8D31&pd_rd_wg=n7VNj&pf_rd_i=desktop-dp-sims&pf_rd_m=ATVPDKIKX0DER&pf_rd_p=56838e6b-66d4-41e0-a762-743f1a1a628a&pf_rd_r=GJBKNFNVWKY6EHZ5SBQH&pf_rd_s=desktop-dp-sims&pf_rd_t=40701&psc=1&refRID=GJBKNFNVWKY6EHZ5SBQH

## Slide 15: Network Fundamentals
Routers

## Slide 16: Network Fundamentals
Wireless access point (WAP)
  Receives and transmits radio signals
  Joins wireless nodes to a wired network

## Slide 17: Network Fundamentals
Server
  Computer or device with software that manages network resources, such as files, e-mails, printers, databases
File server
  Most common type of server
  High-speed computer that provides program and data files to network users
  Contains the network operating system (NOS)
    File directories for file and resource location on the LAN
    Automated distribution of software updates to desktop computers on the WAN
    Internet services support
    Protection of services and data
    Access to connected hardware by authorized users

## Slide 18: Network Fundamentals
Network administrator
  Also called network engineer
  Installs, maintains, supports computer networks
  Interact with users
  Handle security
  Troubleshoot problems

## Slide 19: Advantages - Disadvantages
Advantages
  Reduced hardware costs
  Application sharing
  Sharing information resources
  Data management centralization
  Connecting people
disadvantages
  Loss of autonomy
  Lack of privacy
  Security threats
  Loss of productivity

## Slide 20: Local Area Networks
Local area network (LAN)
  Connects hardware devices that are in close proximity
  The owner of the devices is also the owner of the means of communications
  Common wired LAN topologies
    Bus
    Ring
    Star

## Slide 21: Local Area Networks

## Slide 22: Local Area Networks
Peer-to-peer networks
Wireless LAN
Client/server LAN
Intranet

## Slide 23: Peer-to-peer (P2P) networks
Share files without a file server
Easy to set up
Best used for home or small offices with no more than 10 computers
Do not require a network operating system
Can be slow if there are too many users
Security not strong

## Slide 24: Peer-to-peer (P2P) networks

## Slide 25: Wireless LAN
Connects users through radio waves instead of wires
Use includes networks in:
  Homes
  Hospitals
  Colleges
Secured with a radio transmission technique that spreads signals over a seemingly random series of frequencies.
Effective inside range of between 125 and 300 feet

## Slide 26: Wireless LAN

## Slide 27: Client/server networks
Client/server networks
  Made up of one or more file servers and clients (any type of computer)
  Client software enables requests to be sent to the server
  Wired or wireless connections
  Do not slow down with heavy use

## Slide 28: Client/server networks

## Slide 29: Intranet
Intranet
  Password-protected network controlled by the company
  Accessed only by employees
Virtual private network
  Operates over the Internet
  Accessible by authorized users for quick access to corporate information
  Uses secure, encrypted connections and special software

## Slide 30: LAN topologies
Network topology
  Physical design of a LAN
Topology resolves contention—conflict that occurs when two or more computers on the network attempt to transmit at the same time
Contention sometimes results in collisions—corruption of network data caused when two computers transmit at the same time

## Slide 31: LAN topologies
Bus topology
  Practical for home or small office
  One node transmits at a time
  Terminators signify the end of the circuit
  Uses contention management—technique that specifies what happens when a collision occurs
Star topology
  For office buildings, computer labs, and WANs
  Easy to add users
Ring topology
  For a division of a company or one floor
  Not in common use today
  Node can transmit only when it has the token—special unit of data that travels around the ring

## Slide 32: Local Area Networks

## Slide 33: LAN topologies

## Slide 34: LAN topologies

## Slide 35: LAN technologies
Ethernet—most-used LAN protocol
  Ethernet star networks
    Most popular versions—use twisted-pair wiring and switches
  Sends data in a fixed-size unit called a packet
WiFi
  Uses radio waves to provide a wireless LAN standard at Ethernet speeds
  Needs a central access point—could be a wireless router
  Hot spots—public wireless access locations

## Slide 36
Figure 7.6
An Ethernet LAN Implemented Using a Hub

## Slide 37: Local Area Networks (continued)
Ethernet
  Most widely used LAN technology
  Uses the bus topology
  Two ways to construct an Ethernet LAN
    Shared cable
    Hubs: The most widely used technology

## Slide 38: Protocols
CSMA/CD (Carrier Sense, Multiple Access with Collision Detection)
  Used in Ethernet
  Silent bus provides right to introduce new message
CSMA/CA (Carrier Sense, Multiple Access with Collision Avoidance)
  Used in WiFi
  Hidden terminal problem

## Slide 39: The hidden terminal problem

## Slide 40
Figure 7.5
An Ethernet LAN Implemented
Using Shared Cables

## Slide 41
Figure 7.5
An Ethernet LAN Implemented
Using Shared Cables

## Slide 42: Wide Area Networks

## Slide 43: Wide Area Networks
Wide area networks (WANs)
  Connect devices that are across town, across the country, or across the ocean
  Users must purchase telecommunications services from an external provider
  Dedicated point-to-point lines
  Most use a store-and-forward, packet-switched technology to deliver messages

## Slide 44: Wide Area Networks

## Slide 45: Wide Area Networks

## Slide 46: Wide Area Networks

## Slide 47: Wide Area Networks

## Slide 48: WAN applications
E-mail, conferencing, document exchange, remote database access
LAN to LAN connections connect two or more geographically separate locations
Transaction acquisition—the instant relay of transaction information from a point-of-purchase sale.

## Slide 49
Figure 7.7
Typical Structure of a Wide Area Network

## Slide 50: Figure 4.1 Network topologies

## Slide 51: Figure 4.1 Network topologies (continued)

## Slide 52: Figure 4.2 Communication over a bus network

## Slide 53: Building a large bus network from smaller ones

## Slide 54: Routers

## Slide 55: Inter-process Communication
Client-server
  One server, many clients
  Server must execute continuously
  Client initiates communication
Peer-to-peer (P2P)
  Two processes communicating as equals
  Peer processes can be short-lived

## Slide 56: Figure 4.6 The client/server model compared to the peer-to-peer model

## Slide 57: Distributed Systems
Systems with parts that run on different computers
  Cluster computing
  Grid computing
  Cloud computing
    Amazon’s Elastic Compute Cloud
    Google Drive

## Slide 58: The Internet

## Slide 59: The Internet
The Internet: An internet that spans the world
  Original goal was to develop a means of connecting networks that would not be disrupted by local disasters
  Today a commercial undertaking that links a worldwide combination of PANs, LANs, MANs, and WANs involving millions of computers

## Slide 60: Internet Architecture
Internet Service Provider (ISP)
  Tier-1
  Tier-2
Access or tier-3 ISP: Provides connectivity to the Internet
  Hot spot (wireless)
  Telephone lines
  Cable/Satellite systems DSL
  Fiber optics

## Slide 61: Internet Composition

## Slide 62: Internet Addressing
IP address: pattern of 32 or 128 bits often represented in dotted decimal notation
Mnemonic address:
  Domain names
  Top-Level Domains
Domain name system (DNS)
  Name servers
  DNS lookup

## Slide 63: ICANN
Internet Corporation for Assigned Names & Numbers (ICANN)
Allocates IP addresses to ISPs who then assign those addresses within their regions.
Oversees the registration of domains and domain names.

## Slide 64: Early Internet Applications
Network News Transfer Protocol (NNTP)
File Transfer Protocol (FTP)
Telnet and SSH (Secured Shell)
Hypertext Transfer Protocol (HTTP)
Electronic Mail (email)
  Domain mail server collects incoming mail and transmits outing mail
  Mail server delivers collected incoming mail to clients via POP3 (Post Office Protocol version 3) or IMAP (Internet Mail Access Protocol)

## Slide 65: SMTP Simple Mail Transfer Protocol
220 mail.tardis.edu SMTP Sendmail Gallifrey-1.0; Fri, 23 Aug 2413 14:34:10
HELO mail.skaro.gov
250 mail.tardis.edu Hello mail.skaro.gov, pleased to meet you
MAIL From: dalek@skaro.gov
250 2.1.0 dalek@skaro.gov... Sender ok
RCPT To: doctor@tardis.edu
250 2.1.5 doctor@tardis.edu... Recipient ok
DATA
354 Enter mail, end with "." on a line by itself
Subject: Extermination.
EXTERMINATE!
Regards, Dalek
.
250 2.0.0 r7NJYAEl028071 Message accepted for delivery
QUIT
221 2.0.0 mail.tardis.edu closing connection

## Slide 66: More Recent Applications
Voice Over IP (VoIP)
Internet Multimedia Streaming
  N-unicast
  Multicast
  On-demand streaming
  Content delivery networks (CDNs)

## Slide 67: World Wide Web

## Slide 68: World Wide Web
Hypertext combines internet technology with concept of linked-documents
  Embeds hyperlinks to other documents
Browsers present materials to the user
Webservers provide access to documents
Documents are identified by URLs and transferred using HTTP

## Slide 69: A typical URL

## Slide 70: Hypertext Markup Language (HTML)
Encoded as text file
Contains tags to communicate with browser
  Appearance
    <h1> to start a level one heading
    <p> to start a new paragraph
  Links to other documents and content
    <a href = . . . >
  Insert images
    <img src = . . . >

## Slide 71: A simple webpage

## Slide 72: A simple webpage

## Slide 73: An enhanced simple webpage

## Slide 74: An enhanced simple Web page

## Slide 75: Extensible Markup Language (XML)
XML: A language for constructing markup languages similar to HTML
  A descendant of SGML
  Opens door to a World Wide Semantic Web

## Slide 76: Using XML
<staff clef = "treble"> <key>C minor</key>
<time> 2/4 </time>
<measure> <rest> egth </rest> <notes> egth G, egth G, egth G </notes></measure>
<measure> <notes> hlf E </notes></measure>
</staff>

## Slide 77: Client Side Versus Server Side
Client-side activities
  Javascript
  Macromedia Flash
Server-side activities
  Common Gateway Interface (CGI)
  Servlets
  JavaServer Pages (JSP) / Active Server Pages (ASP)
  PHP

## Slide 78: Package-shipping example

## Slide 79: Internet Software Layers
Application: Constructs message with address
Transport: Chops message into packets
Network: Handles routing through the Internet
Link: Handles actual transmission of packets

## Slide 80: The Internet software layers

## Slide 81: A message through the Internet

## Slide 82: TCP/IP Protocol Suite
Transport Layer
  Transmission Control Protocol (TCP): break down messages or files into smaller pieces (called packets). When receiving, reassembles the data into a complete file or message. provide error-checking if an error is found TCP retransmits the packet(s).
  User Datagram Protocol (UDP): UDP does not divide each transmission into packets, which allows for a faster transmission. does not provide error checking.
Network Layer
  Internet Protocol (IP)
    IPv4
    IPv6

## Slide 83: Choosing between TCP and UDP

## Slide 84: Security

## Slide 85: Security
Attacks
  Malware (viruses, worms, Trojan horses, spyware, phishing software)
  Denial of service (DoS)
  Spam
Protection
  Firewalls
  Spam filters
  Proxy Servers
  Antivirus software

## Slide 86: Types of computer crime
Identify theft—criminal access to personal information in order to impersonate someone
Dumpster diving—disgruntled employees or thieves go through a company’s trash to find information they can steal
Phishing attacks—legitimate-looking e-mails or Web sites created in an attempt to obtain confidential data about a person
Spear phishing (similar to phishing)—uses targeted fake e-mails and social engineering to trick recipients into providing personal information to enable identity theft

## Slide 87: Types of computer crime
Malware (short for malicious software)—programs that intentionally harm a computer system or allow individuals to gain access without permission
  Tips to protect yourself from malware:
    Know who you are dealing with
    Keep your Web browser and operating system up to date
    Back up important files
    Protect children online
    Use security software tools and keep them up to date
    Use strong passwords
    Learn what to do if something goes wrong

## Slide 88: Types of computer crime
Spyware—software that gathers private information and tracks Web use
  Adware—form of spyware that generates annoying pop-up and banner ads
  Keyloggers—record keystrokes to provide cybercriminals with confidential data

## Slide 89: Types of computer crime
Computer virus—code concealed inside a program that can harm or destroy files
  Many spread through e-mail attachments
  File infectors—attach themselves to files
  Payload—refers to the dangerous actions a virus performs.
  Macro viruses—attach to data files and take advantage of application macros
  Boot sector viruses—execute each time you start the computer
  SPIM—spam text message sent via a cell phone or instant messaging service

## Slide 90: Computer Crime and Cybercrime

## Slide 91: Types of computer crime
Rogue programs
  Logic bomb—hidden computer code that sits dormant on a system until triggered
  Time bomb—virus program that remains dormant on a computer system until activated
  Worm—similar to a virus but does not need action of a user to execute

## Slide 92: Types of computer crime
Denial of service (DoS) attack—assaults an Internet server with so many requests it can’t function
  Distributed denial of service (DDoS)—attack involves multiple computer systems
    Commandeered computers form a botnet (robot network)
    Bot (short for robot)—connects individual computers to the controller, usually a server under the control of the botnet controller
    The individual computers are called zombies.

## Slide 93: Computer Crime and Cybercrime
More rogue programs (con’t.)
  Syn flooding—form of denial of service attack in which synchronization packets are repeatedly sent to every port on the server
    Uses up all available network connections
    Locks them until they time out
  Rootkit—malicious program that is disguised as a useful program
    Enables attacker to gain administrator level access
    Allows attacker to have repeated and undetected access
  Trojan horse—normal-looking program that includes concealed instructions to cause harm

## Slide 94: Computer Crime and Cybercrime
Fraud, theft, and piracy
  Memory shaving
  Software piracy
Cybergaming crime
Tricks for obtaining passwords
Salami shaving and data diddling
Forgery

## Slide 95: Encryption
HTTPS and SSL
Public-key Encryption
  Public key: Used to encrypt messages
  Private key: Used to decrypt messages
Certificates and Digital Signatures
  Certificate authorities

## Slide 96: Public-key encryption

## Slide 97: Computer crime

## Slide 98: Computer Crime
cyber crime, e-crime, electronic crime, or hi-tech crime.
Computer crime is an act performed by a knowledgeable computer user, sometimes referred to as a hacker that illegally browses or steals a company's or individual's private information.
In some cases, this person or group of individuals may be malicious and destroy or otherwise corrupt the computer or data files.

## Slide 99: Computer crime
Child pornography - Making or distributing child pornography.
Copyright violation - Stealing or using another person's copyrighted material without permission.
Cracking - Breaking or deciphering codes that are being used to protect data.
Cyber terrorism - Hacking, threats, and blackmailing towards a business or person.
Cyberbully or Cyberstalking - Harassing or stalking others online.
Cybersquatting - Setting up a domain of another person or company with the sole intentions of selling it to them later at a premium price.
Creating Malware - Writing, creating, or distributing malware (e.g., viruses and spyware.)
Denial of Service attack - Overloading a system with so many requests it cannot serve normal requests.
Espionage - Spying on a person or business.
Notes: Espionage: gián điệp
Squatt: câu/mồi
malware: malicious software

## Slide 100: Computer crime
Fraud - Manipulating data, e.g., changing banking records to transfer money to an account or participating in credit card fraud.
Harvesting - Collect account or other account related information on other people.
Human trafficking - Participating in the illegal act of buying or selling other humans.
Identity theft - Pretending to be someone you are not.
Illegal sales - Buying or selling illicit goods online including drugs, guns, and psychotropic substances.
Intellectual property theft - Stealing practical or conceptual information developed by another person or company.
IPR violation - An intellectual property rights violation is any infringement of another's copyright, patent, or trademark.
Phishing - Deceiving individuals to gain private or personal information about that person.

## Slide 101: Computer crime
Salami slicing - Stealing tiny amounts of money from each transaction.
Scam - Tricking people into believing something that is not true.
Slander - Posting libel or slander against another person or company.
Software piracy - Copying, distributing, or using software that is copyrighted that you did not purchase.
Spamming - Distributed unsolicited e-mail to dozens or hundreds of different addresses.
Spoofing - Deceiving a system into thinking you are someone you really are not.
Typosquatting - Setting up a domain that is a misspelling of another domain.
Unauthorized access - Gaining access to systems you have no permission to access.
Wiretapping - Connecting a device to a phone line to listen to conversations.
Notes: Samali slicing: samali (xúc xích Ý)/cut to small fraction
Scam: mưu đồ bất lương
Slander: vu khống/vu cáo/phỉ bang
Spoof: bắt chước
Deceive: lừa gạt

## Slide 102: Cyberbully
Alternatively referred to as a cyberstalker, a cyberbully is someone who posts inappropriate or unwanted things about another person, or otherwise harasses them in e-mails, IMs, or SMS.

## Slide 103: Spyware
Spyware or snoopware
  a software program that is intentionally installed on a computer by to monitor what other users of the same computer are doing.
  a program designed to gather information about a user's activity secretly. Spyware programs are often used to track users' habits to target them with advertisements better.

## Slide 104: Computer fraud
Computer fraud
  any act using computers, the Internet, Internet devices, and Internet services to defraud people, companies, or government agencies of money, revenue, or Internet access.
  Illegal computer activities include phishing, social engineering, viruses, and DDoS attacks are some examples used to disrupt service or gain access to another's funds.
Notes: Fraud: lừa gạt /frod/
Defraud: giành cho được

## Slide 105: Identity theft
Identity theft is the act of a person obtaining information illegally about someone else.
Thieves try to find such information as full name, maiden name, address, date of birth, social security number, passwords, phone number, e-mail, and credit card numbers.
The thief can then use this information to gain access to bank accounts, e-mail, cell phones, identify themselves as you, or sells your information.

## Slide 106: Phishing
describe a malicious individual or group of individuals who scam users.
They do so by sending e-mails or creating web pages that are designed to collect an individual's online bank, credit card, or other login information. Because these e-mails and web pages look like legitimate companies users trust them and enter their personal information.

## Slide 107: Quiz

## Slide 108: Quiz
Which of the following best describes the Internet?
A network of interlinked computers
A communications network
An information network
All of the above
Notes: Answer: d All of the above. The Internet is a network of interlinked computers accessible worldwide. It facillitates communication by way of email, forums, chatrooms and blogs and hosts information and content ranging from online newspapers to wikis.

## Slide 109: Quiz
When was the first Internet network started?
1969
1983
1987
1996
Notes: Answer: a The first Internet started in 1969. It started as a series of networked computers set up at The University of California, Los Angeles, called ARPANET. The first node was switched on on October 29, 1969. In 1983 the Internet was created over a wide network area when the US National Science Foundation created a university wide net NSFnet.

## Slide 110: Quiz
The Internet was originally developed by whom?
computer hackers
corporation
the U.S. Department of Defense
the University of Michigan

## Slide 111: Quiz
Where do files live on the Internet?
On your computer
On one massive computer - the www
On individual computers, often known as servers
On a network of routers
Notes: Answer: c Files on the Internet live on individual computers, often known as servers. A server can be a computer or software running on a computer that provides services to other computers, such as hosting Internet files. A server can also act as a client, requesting and viewing web pages.

## Slide 112: Quiz
Who writes the rules for the Internet?
No-one
The government of the country in which the Internet is being used
The Internet Society
Your parents
Notes: Answer: a No-one. The Internet is not governed by any one body. The Internet Society works to create standards for the Internet, such as which standard of Internet Protocol (IP) is used. In countries such as China the government uses software to block certain sites and sections of the net. Children may also have their access to the net limited by their parents.

## Slide 113: Quiz
Which of the following is a TRUE statement?
You are free to copy information you find on the Web and include it in your research report.
You do not have to cite the Web sources you use in your research report.
You should never consult Web sources when you are doing a research report.
Just like print sources, Web sources must be cited in your research report. You are not free to plagiarize information you find on the Web.

## Slide 114: Quiz
What is the World Wide Web?
computer game
software program
the part of the Internet that enables information-sharing via interconnected pages
another name for the Internet

## Slide 115: Quiz
What does URL stand for?
Unique Records List
Uniform Resource Locator
Undefined Restricted Learner
Universal Robot Location
Notes: b) Uniform Resource Locator.

## Slide 116: Quiz
Which of the following is used to translate between IP addresses and mnemonic addresses?
File server
Mail server
Name server
FTP server

## Slide 117: Quiz
Which of the following is not a means of connecting networks?
Switch
Server
Router
Bridge

## Slide 118: Quiz
Which of the following is not an email related protocol?
HTTP
POP3
IMAP
SMTP